## Slide 1: Challenge 1: Temperature Sensing EC 544 – Fall 2015
Group 4: Lama, Dung, Hitesh, Yisi, Weilun

## Slide 2: Solution Architecture
Central Station
Sensor 1
Sensor 2
Sensor 3
Sensor 4
Sensor Components
Thermistor Circuit (voltage divider)
XBee Router
Arduino Board
XBee Coordinator
Computer
Central Station Components

## Slide 3: Data Flow
Sketch calculates Temp
XBee Router sends data to Central St.
Sleep for 5 min (Power Saving)
Arduino reads analog voltage
XBee Coordinator receives temp from all sensors
JS script calculates avg temp
Output avg temp to web interface
Sensor Side
Central Station Side

## Slide 4: Calibration
Thermistor
Variable Resistance
Reads only Voltage
That is why we used a Voltage Divider circuit.
Steps to Calculate
Temperature
Back calculate the Resistance Rt from the Voltage V₀ using
Rt = R*( 1023.0 / Vo - 1.0 )
Once we have the resistance Rt we can easily get the temperature with the Steinhart Equation:

## Slide 5: Design Decisions
Data Processing:
  Sensors: Calculate Temperatures
  Central Station: Stores latest values for each sensors and calculates average
Sampling Interval:
  Every 5 min.
Sensor Positioning:
  Within the XBee range
Power Consumption:
  Set Arduino to sleep mode in between intervals

## Slide 6: Challenges & Future Improvements
Challenges:
  Learning how to use and integrating different platforms
  Calibration: getting accurate readings and calculating the SH coefficients
Future Improvements:
  Averaging Algorithm:
  - Improve to handle sensor malfunctions/outliers
  - Improve to give weight to each sample depending on sensor location
  Data Storage:
  - Store data so that it can be later retrieved and visually represented