## Slide 1: Challenge 4: Steering the Car EC 544 – Fall 2015
Group 4: Dung, Hitesh, Lama, Yisi, Weilun

## Slide 2: Solution Architecture
Arduino
xBee
Speed Sensor
LIDARLite
UltraSonic

## Slide 3: Design Decisions
Sensor:
  1 LIDAR sensor on the side:
    Accurate response (not much of noise)
    Rapid response
  2 Ultrasonic sensor in the front:
    Scalable
    Effective in detecting corners and small obstacles
  1 IR speed sensor on inner side of wheel:
    Sensitive to colors, can be used to calculate angular velocity
    Helpful in remote control

## Slide 4: Design Decisions
  Control Algorithms:
  Side
    PID algorithm
    Adapt the output to adjust the wheel direction
  Front
    Receive value from the two sensors and stop if either of them senses obstacle ahead
  Speed
    Rotary encoder, sense the color wheel inside of the wheel
  Remote: xBee
    Sending start/stop commands
    Monitoring the speed via xBee

## Slide 5: Challenges & Future Improvements
Challenges:
  Choosing the proper sensors to use and interfacing them together on Arduino
  Dealing with limitations of each sensor, calibrating the out puts
  Learning to use PID libraries an testing on combination of PID coefficients
Future Improvements:
  Make the crawler adaptive to different environment:
    Make turns,etc.
  Better remote control:
    Change speed, make turns, etc.

## Slide 6: Thank You!