## Slide 1: Challenge 4: Steering the Car EC 544 – Fall 2015
Group 4: Dung, Hitesh, Lama, Yisi, Weilun

## Slide 2: Solution Architecture
Arduino
xBee
Photoreflector (Speed Sensor)
LIDARLite
Sensor
Ultrasonic
Sensor
Arduino
xBee
Front

## Slide 3: Design Decisions
Sensors:
  1 LIDAR sensor on the side:
    Accurate measure
    Rapid response
  1 Ultrasonic sensor in the front:
    Effective in detecting obstacles ahead
    Scalable (easy to use multiples if needed)
  1 Photoreflector on inner side of wheel:
    Sensitive to colors, can be used to calculate angular velocity
    Can be helpful in remote control

## Slide 4: Design Decisions
  Control Algorithms:
  Side
    PID: Distance to wall control
    Adapt the output to adjust the wheel direction
  Front
    Read data from the ultrasonic sensor and stop if obstacle ahead
  Speed
    Rotary encoder, sense the color wheel inside of the wheel
  Remote: XBee
    Using two PAN IDs:
      Send start/stop commands
      Monitor the speed

## Slide 5: Challenges & Future Improvements
Challenges:
  Choosing the appropriate sensor for each task and calibrating their outputs
  Using the PID library and testing for the right combination of PID coefficients
  Calculating the speed of the wheel (issue with interrupt pins in lead to less accurate results)
  Using the XBee to both send data and receive commands
Future Improvements:
  Make the crawler adaptive to different environments:
    Taking turns
  Better remote control:
    Changing speed, turning , combining Xbee send/receive

## Slide 6: Thank You!