## Slide 1: Challenge 6: Infectious Swarm! EC 544 – Fall 2015
Group 4: Dung, Hitesh, Lama, Yisi, Weilun

## Slide 2
id (1, 2, 3, 4…)
leader (true/false)
infected (true/false)
command (C / I / N)
immunity_interval (ms)
alive_time[]
Software Architecture

## Slide 3: Design Decisions
  Leader Election
    Assign every device an ID
    Leader is the device with lowest ID
    To be a candidate for leader, the device has to be online for at least the last 15 seconds, otherwise it is not considered to be on the network anymore
  Use of XBee’s API vs AT mode
    Implemented the same algorithm using both modes
    AT mode showed better performance (less latency)
    Use of Timer Interrupts
    Used a timer to trigger the sending of messages
    Fewer messages sent  less congested network  better response time
  Command Message
    Each character is a single message, a device may send multiple messages at each interrupt

## Slide 4: Challenges & Future Improvements
Challenges
  Learning about leader election algorithms
  Learning how implement bi-directional communication in API mode
  Having to implement the algorithm in both API and AT modes
  Resolving unexpected behavior when integrating all components (Example: use of sprintf and timer and Xbee's API/AT mode)
Future Improvements
  Faster leader election when leader goes offline
  Faster prorogation of “clear” message when clearing an infection

## Slide 5: Thank You!